## Slide 1: Control and Coordination of Multi-Drone Systems Using Graph Neural Networks
Masters Thesis Defense
By
Parth Khopkar
April 15, 2021

## Slide 2
Warehouse robots
Delivery robots
Delivery drones
Drone light show (Intel)
Notes: As these systems of robots become more prevalent, it is important to study and understand how to improve control strategies for them and coordinate their actions
My thesis focuses on a particular approach to do this with drones

## Slide 3
What?
Collection of autonomous mobile robots working together to achieve a common objective
Coordinate their actions with each other to achieve a task that would be difficult for a single robot.
Why?
Multiple robots introduces redundancy
We want multi-robot systems for the same reason why humans collaborate – to achieve bigger goals than any single one of us can.
Notes: Having seen the what and why, my thesis focuses on one way on “how” to do this

## Slide 4: Constraints on MRS
According to Cortés and Egerstedt (2017), a MRS should satisfy following properties:
Local
Safe
Emergent
Scalable
Notes: Local – individual robots can only act on information available to them
Safe – Robots should be safe from harm that might come from events such as collisions among themselves or environment
Emergent – Global properties should emerge from local interaction rules
Scalable – The algorithm used to control a single robot should not depend on the size of the entire team
I consider the principles as guiding principles while developing the proposed approach

## Slide 5: Challenges in development and use
Earliest approaches used behaviors and functions handcrafted by experts.
With the advent of DL, NNs have been used as function approximators
Learning from scratch is expensive and often unfeasible for real multi-robot systems
Need to generalize and make the controller robust to real world challenges such as noise.

## Slide 6: Imitation Learning with Boids model
Cohesion
Separation
Alignment
Obstacle Avoidance
Goal seeking
Simulate the aggregate motion of a flock of animals
Behavior of each member of the flock is the result of interactions with their neighbors.
The acceleration generated by each member is superimposed to get the final acceleration of each boid
Our aim is to use the trajectories generated by this model to fly drone in a simulator
Interactions in the Boids model
[Reynolds ‘87]
Notes: Was developed by By Reynolds (1987 as a way to simulate a natural flock in computer animation as an alternative to scripting the behavior of individual members of the flock. The original paper referred to these simulated bird like or ”bird-oid” objects as ”boids”.

## Slide 7: PyBullet Physics based simulator
Gym environment based on PyBullet for multi-agent learning with quadrotors
Gym interface allows for greater control over observations and actions
Support for realistic collisions
Comes with support for trajectory tracking and PID control
Notes: PID control allows us to focus on high level behaviors. It takes care of drone flight dynamics Be on the lookout for the yellow rubber duck

## Slide 8: Why not other simulators
RotorS
ROS and Gazebo based simulator
Not parallelizable
AirSim
UE4 based simulator
Tight coupling between rendering and dynamics (no headless mode)
Flightmare
Unity based photorealistic simulator
Parallelizable
No support for multi-agent interfaces
Notes: Flightmare is close but no multi-agent interface is a deal breaker

## Slide 9: Graph Neural Networks (GNNs)
Function approximators that operate on graph-based data
Explicitly model the interaction dynamics of the entities present in the graphs
Used in areas with rich relational structures – Physics, Molecular Chemistry, Traffic Networks etc.
What makes them attractive – permutation invariance, locality
Input
Output
Graph
Neural
Network
Notes: Need for inductive biases
Inductive biases in GNNs and how they help capture the intuition in MRS
Permutation invariant
locality

## Slide 10
Convolutional Neural Networks (CNNs)
Operate on Euclidean spatial data
Recurrent Neural Networks (CNNs)
Operate on temporal data
NN structures produce inductive biases
Inductive biases in deep learning help to form better representations
It is easier to pick a good solution when there is less ambiguity

## Slide 11: GNN operations
(1)
(2)
(3)
(4)
: Edge state
: Edge function
: Neighborhood of node
: Read out function
: Node state
: Node function
: Node embedding
: Desired output
Based on SwarmNet architecture by Zhou et al. (2019)
Notes: Message Passing Neural Network

## Slide 12: How GNNs model MRS
Graph
Neighborhood of node:
Edges of type where (obstacle, goal and boid)
MLP approximators - , ,
obstacle
goal
boid
obstacle
goal
boid
Notes: MRS due to their interactions can naturally be modelled as graphs

## Slide 13: Trajectories in Boids model
Dimension: (Time steps Number of entities Dimension)
State vector (coordinate and velocity vectors)
Sample Boids trajectories
Notes: We sample states from the Boids model at discrete time steps to from the trajectories

## Slide 14: Loss function
MSE loss normalized by ()
Normalization rectifies dependence of error on sampling frequency of the trajectory

## Slide 15: Training and Inference
Training
Repeatedly train the model on the trajectories with increasing prediction horizon
  e.g. For 36 step trajectory, model is trained for prediction steps = 1, 2, 4, 8, 16
This is necessary to ensure that the GNN learns to faithfully clone Boids model
Inference
Single step prediction based on current state is used as input to PID controller

## Slide 16: Network Architecture
+

## Slide 17: System Architecture
Graph Neural Network
Controller
PID controller
Agent
states
Context
Next state
Velocity
Updated states in the simulator
Predict

## Slide 18: Results on direct transfer
The GNN based controller is capable of controlling drones directly after
Imitation Learning training
Notes: Drones are able to generalize to varying positions of the obstacles

## Slide 20: Parameter differences
Important to adjust key parameters between Boids trajectories and PyBullet simulator
Importance of stepping frequency
  Low frequency in Boids trajectory captures same behaviors in fewer steps
Avoiding collisions in PyBullet simulator by adjusting size
  Size of boid in training data is kept high since size is more of a “comfortable distance” for the Boids model
36 steps
575 steps

## Slide 21: Reward function
To quantify the performance of the drones in the simulator, following reward function is used:
Large cost for collision
Distance between
Drone and
Size of drone
Size of obstacle

## Slide 22: Scalability
GNNs provide scalability by default as opposed to other approaches
  Possible since the update equations of GNNs do not depend on size of graph
  Due to the poor ability of MLPs to extrapolate, the performance degrades
Controller trained on N=5 drones tested on more drones
Notes: Important to understand this performance

## Slide 23
N = 5
N = 6
N = 7
N = 8
N = 9
Notes: Drones are not able to navigate as well but underlying behaviors of Boids model are still visible. No collisions

## Slide 24: Robustness
In real life scenarios, sensor noise is bound to be present
  Due to communication issues
  Due to presence of adversarial elements
Experiments with distributed control and noise
  Each drone receives perfect observations for own state but noisy observations for all other entities in the environment
To combat noise, controller was trained on Boids trajectories with randomly sampled Gaussian noise
Controller trained with noise shows a more graceful performance degradation but gets lower reward overall
It learns to take more conservative paths

## Slide 25
Controller trained without noise
Controller trained with noise
Both controllers tested on noise with std = 0.8

## Slide 26: Reinforcement Learning for combating noise
Reinforcement Learning on Imitation Learning trained controller
  Idea: Since IL has already learned correct behaviors, use RL to teach it how to deal with noise
  Use Proximal Policy Optimization (PPO) algorithm for RL
  Lock edge MLP and pretrain value function using IL policy self-play
  Start training process keeping locked
Notes: We can take advantage of the function separation in GNNs

## Slide 27
Results
  The reward is initially high because of IL trained policy
  As training goes on, RL erodes behaviors learnt during IL, leading to performance drop
Directly using Reinforcement Learning after Imitation Learning is not ideal for our use case because:
  It is counter-intuitive to let the controller forget and learn new behaviors
  For use cases such as flying drones which is non-ergodic, it is imperative that the initial training performance is not poor.
Intuition
  Switching the learning signal from supervised loss to reward signal (which are inherently different mathematical signals) causes divergence
Possible solution
  Use demonstrations along with collected experience during Reinforcement Learning
Notes: But we leave that as future work

## Slide 28: Summary
GNNs can be used to leverage the problem structure inherent in Multi-Robot Systems
Imitation Learning combined with GNNs can be used to directly control drones in a Physics based simulator
The proposed approach is capable of scaling up and dealing with sensor noise to some extent

## Slide 29: Future Work
Deploying on real drones
Exploring challenges for real life applications such as target location
Adding vision perception capabilities
Exploring how a more sophisticated approach to Reinforcement Learning combined with demonstration data can help better deal with noise

## Slide 30: Thank You